## Slide 1: Electrical Circuits Lecture 1: Introduction By: Mahmoud Momtazpour ceit.aut.ac.ir/~momtazpour
Amirkabir University of Technology

## Slide 2: Textbook
C. Desoer, Basic Circuit Theory, 2nd Edition
W. Hayt, Engineering Circuit Analysis, 8th Edition
A. Agarwal, Foundations of Analog and Digital Electronic Circuits

## Slide 3: SI: Units and Prefixes
Any measurement can be expressed in terms
of a unit, or a unit with a “prefix” modifier.
Example: 12.3 mW = 0.0123 W =1.23 x 10-2 W
FACTOR | NAME | SYMBOL
10-9 | nano | n
10-6 | micro | μ
10-3 | milli | m
103 | kilo | k
106 | mega | M
Notes: SI: International system of units: سیستم واحد گذاری بین المللی
یک استاندارد برای اندازه گیری جرم، حجم، طول و ...

## Slide 4: Charge
charge is conserved: it is neither created nor destroyed
symbol: Q or q; units are coulomb (C)
the smallest charge, the electronic charge, is carried by an electron (−1.602×10-19 C) or a proton (+1.602×10-19 C)
in most circuits, the charges in motion are electrons

## Slide 5: Current and Charge
Current is the rate of charge flow:
1 ampere = 1 coulomb/second (or 1 A = 1 C/s)

## Slide 6: Current and Charge
Current (designated by I or i) is the rate of flow of charge
  i=dq/dt
Current must be designated with both a direction and a magnitude
These two currents are the same:

## Slide 7: Current and Charge: i=dq/dt
Notes: بار در ثانیه 4 صفر است، ولی جریان 1.5. معنی آن چیست؟

## Slide 8: Voltage
When 1 J of work is required to move 1 C of charge from A to B, there is a voltage of 1 volt between A and B.
  V = dW/dq
Voltage (V or v) across an element requires both a magnitude and a polarity.
Example: (a)=(b), (c)=(d)

## Slide 9: Power: p = v i
The power required to push a current i (C/s) into a voltage v (J/C) is p = vi ( J/s = W).
When power is positive, the element is absorbing energy.
(Passive element)
When power is negative, the element is supplying energy.
(Active element)

## Slide 10: Example: Power
How much power is absorbed by the three elements above?
Pa = + 6 W, Pb = +6 W, Pc = -20 W.
(Note: (c) is actually supplying power)
Notes: جهت قراردادی با ارائه یک مثال از سه دانشجو که جهتهای متفاوتی می گیرند و تاثیر آن بر محاسبه توان مصرفی یا تولیدی

## Slide 11: Circuit Elements
A circuit element usually has two terminals (sometimes three or more).
The relationship between the voltage v across the terminals and the current i through the device defines the circuit element model.

## Slide 12: Voltage Sources
An ideal voltage source is a circuit element that will maintain the specified voltage vs across its terminals.
The current will be determined by other circuit elements.

## Slide 13: Current Sources
An ideal current source is a circuit element that maintains the specified current flow is through its terminals.
The voltage is determined by other circuit elements.

## Slide 14: Battery as a Voltage Source
A voltage source is an idealization (no limit on current) and generalization (voltage can be time-varying) of a battery.
A battery supplies a constant “dc” voltage V but in practice a battery has a maximum power.

## Slide 15: Dependent Sources
Dependent current sources (a) and (b) maintain a current specified by another circuit variable.
Dependent voltage sources (c) and (d) maintain a voltage specified by another circuit variable.

## Slide 16: Example: Dependent Sources
Find the voltage vL in the circuit below.

## Slide 17: Ohm’s Law: Resistance
A (linear) resistor is an element for which
v=Ri
where the constant R is a resistance.
The equation is known as “Ohm’s Law.”
The unit of resistance is ohm (Ω).

## Slide 18: Ohm Law Visualization

## Slide 19: Resistors
typical resistors (b) power resistor
(c) a 10 TΩ resistor (d) circuit symbol

## Slide 20: The i-v Graph for a Resistor
For a resistor, the plot of current versus voltage is a straight line:
In this example, the slope is 4 A / 8 V or 0.5 Ω-1.
This is the graph for a 2 ohm resistor.
R=?

## Slide 21: Power Absorption
Resistors absorb power: since v=iR
p=vi = v2/R = i2R
Positive power means the device is absorbing energy.
Power is always positive for a resistor!
Notes: المانهای پسیو (غیر فعال) مانند سیم، مقاومت و دیود خطی و ... نمی توانند مقاومت مطلق (R=v/i) منفی داشته باشند. برای داشتن مقاومت منفی، المان باید اکتیو باشد مانند منبع تغذیه و باتری، که در مورد آنها واژه مقاومت خیلی کاربردی نیست و عملا استفاده نمی شود.
جالب است بدانید که مفهومی به نام مقاومت تفاضلی نیز وجود دارد که به صورت R=dv/di تعریف می شود. در برخی المانهای غیرخطی مانند تقویت کننده ها و لامپ خلاء و برخی انواع دیودهای غیر خطی، مقدار این مقاومت می تواند منفی باشد.

## Slide 22: Example: Resistor Power
A 560 Ω resistor is connected to a circuit which causes a current of 42.4 mA to flow through it.
Calculate the voltage across the resistor and the power it is dissipating.
v = iR = (0.0424)(560) = 23.7 V
p = i 2R = (0.0424)2(560) = 1.007 W

## Slide 23: Wire Gauge and Resistivity
The resistance of a wire is determined by the resistivity of the conductor as well as the geometry:
R = ρ l / A
[In most cases, the resistance of wires can be assumed to be 0 ohms.]

## Slide 24: Conductance
We sometimes prefer to work with the reciprocal of resistance (1/R), which is called conductance (symbol G, unit siemens (S)).
A resistor R has conductance G=1/R.
The i-v equation (i.e. Ohm’s law) can be written as
i=Gv
Notes: رسانایی یا کانداکتنس، معکوس مقاومت است و نشان می دهد یک المان چقدر هادی خوبی برای جریان است.

## Slide 25: Open and Short Circuits
An open circuit between A and B means i=0.
Voltage across an open circuit: any value.
An open circuit is equivalent to R = ∞ Ω.
A short circuit between A and B means v=0.
Current through a short circuit: any value.
A short circuit is equivalent to R = 0 Ω.

## Slide 26: Circuit Component
Circuit Components
Linear
Time-Variant
Time-Invariant
Nonlinear
Time-Variant
Time-Invariant

## Slide 27: Linear vs. Nonlinear
f(x) is linear iff:
  f(x1+x2)=f(x1)+f(x2)
  f(ax)=af(x)
Linear resistor
  v = f(i) = 2 i
Nonlinear resistor
  v = f(i) = 50 i + 0.5 i3
  E.g. Diodes, Neon Lamps
Nonlinear
Linear

## Slide 28: Time-variant vs. Time-Invariant
Example:
Time-invariant resistor
  v(t) = R i(t) , R = constant
Time-variant resistor
  v(t) = R(t) i(t), R(t) = Ra + Rbcos2𝜋ft
  E.g. Potentiometer

## Slide 29: Summary
Electrical circuits concepts
Charge, Current, Voltage, Power, Energy
Voltage/Current Sources
Resistor as the simplest element of Elec. Circuits
  V=RI
  G=1/R
  P=VI=RI2
Active vs. Passive elements
Linear/Nonlinear, Time Variant/Invariant

## Slide 30: In-class Exercise
Find the power absorbed by each element in the circuit
(left to right) −56 W; 16 W; −60 W; 160 W; −60 W.

## Slide 31: In-class Exercise 2
Compute I and PR for each figure

## Slide 32: In-class Exercise 2
Compute VR2 as a function of VS, R1 and R2.