## Slide 1: Electrical Circuits Lecture 4: Handy Circuit Analysis Techniques By: Mahmoud Momtazpour ceit.aut.ac.ir/~momtazpour
Amirkabir University of Technology

## Slide 2: Topic Overview
Handy Circuit Analysis Techniques
  Superposition Concept
  Practical Source
  Source Transformation
  Thevenin/Norton Circuits
  Δ-Y Conversion

## Slide 3: The Superposition Concept
For the circuit shown, the solution can be expressed as:
Question: How much of v1 is due to source A, and how much is because of source B?
We use the superposition principle to answer.

## Slide 4: The Superposition Concept
If we define A as
then
Experiment B
Experiment A
Superposition:
the response is the sum of experiments A and B.

## Slide 5: The Superposition Theorem
In a linear network, the voltage across or the current through any element may be calculated by adding algebraically all the individual voltages or currents caused by the separate independent sources acting “alone”, i.e. with
  all other independent voltage sources replaced by short circuits and
  all other independent current sources replaced by open circuits.
Answer: i3(t) = 1.333 sin t V

## Slide 6: Applying Superposition
Leave one source ON and turn all other sources OFF:
  voltage sources: set v=0.
  These become short circuits.
  current sources: set i=0.
  These become open circuits.
  Find the response from this source.
Add the resulting responses
to find the total response.

## Slide 7: Superposition Example (part 1 of 4)
Use superposition to solve for the current ix

## Slide 8: Superposition Example (part 2 of 4)
First, turn the current source off:

## Slide 9: Superposition Example (part 3 of 4)
Then, turn the voltage source off:

## Slide 10: Superposition Example (part 4 of 4)
Finally, combine the results:

## Slide 11: Example: Power Ratings
Determine the maximum positive current to which the source Ix can be set before any resistor exceeds its power rating.
Answer: Ix<42.49 mA

## Slide 12: Example: Power Ratings

## Slide 13: Superposition with a Dependent Source
When applying superposition to circuits with dependent sources, these dependent sources are never “turned off.”

## Slide 14: Superposition with a Dependent Source
current source off
voltage source off
ix = ix’+ix’’= 2 + (−0.6) = 1.4 A

## Slide 15: Practical Voltage Sources
Ideal voltage sources: a first approximation model for a battery.
Why do real batteries have a current limit and experience voltage drop as current increases?
Two car battery models:

## Slide 16: Practical Source: Effect of Connecting a Load
For the car battery example:
VL = 12 – 0.01 IL
This line represents all possible RL
increase RL

## Slide 17: Practical Voltage Source
The source has an internal resistance or output resistance, which is modeled as Rs
short circuit current (when RL=0)
open circuit voltage (when RL=∞)

## Slide 18: Practical Current Source
The source has an internal parallel resistance which is modeled as Rp
short circuit current (when RL=0)
open circuit voltage (when RL=∞)

## Slide 19: Source Transformation and Equivalent Sources
The sources are equivalent if?
Rs=Rp and vs=isRs

## Slide 20: Source Transformation
The circuits (a) and (b) are equivalent at the terminals.
If given circuit (a), but circuit (b) is more convenient, switch them!
This process is called
source transformation.

## Slide 21: Example: Source Transformation
We can find the current I in the circuit below using source transformation, as shown.
I = (45-3)/(5+4.7+3) = 3.307 mA

## Slide 22: Thévenin Equivalent Circuits
Thévenin’s theorem: a linear network can be replaced by its Thévenin equivalent circuit, as shown below:

## Slide 23: Thévenin Equivalent using Source Transformation
We can repeatedly apply source transformation on network A to find its Thévenin equivalent circuit.
This method has limitations- not all circuits can be source transformed.

## Slide 24: Finding the Thévenin Equivalent
Disconnect the load.
Find the open circuit voltage voc
Find the equivalent resistance Req of the network with all independent sources turned off.
Then:
VTH=voc and
RTH=Req

## Slide 25: Thévenin Example

## Slide 26: Norton Equivalent Circuits
Norton’s theorem: a linear network can be replaced by its Norton equivalent circuit, as shown below:

## Slide 27: Finding the Norton Equivalent
Replace the load with a short circuit.
Find the short circuit current isc
Find the equivalent resistance Req of the network with all independent sources turned off.
Then:
IN=isc and RN=Req

## Slide 28: Source Transformation: Norton and Thévenin
The Thévenin and Norton equivalents are source transformations of each other!
RTH=RN =Req and vTH=iNReq

## Slide 29: Example: Norton and Thévenin
Find the Thévenin and Norton equivalents for the network faced by the 1-kΩ resistor.
Answer: next slide
the load resistor
this is the circuit we will simplify

## Slide 30: Example: Norton and Thévenin
Norton
Thévenin
Source Transformation

## Slide 31: Thévenin Example: Handling Dependent Sources
One method to find the Thévenin equivalent of a circuit with a dependent source: find VTH and IN and solve for RTH=VTH / IN
Example:

## Slide 32: Thévenin Example: Handling Dependent Sources
Finding the ratio VTH / IN fails when both quantities are zero!
Solution: apply a test source.

## Slide 33: Thévenin Example: Handling Dependent Sources
Solve: vtest =0.6 V, and so RTH = 0.6 Ω

## Slide 34: Maximum Power Transfer
What load resistor will allow the practical source to deliver the maximum power to the load?
Answer: RL=Rs
[Solve dpL/dRL=0.]
[Or: pL=i(vs-iRs), set dpL/di=0 to find imax=vs/2Rs. Hence RL=Rs]

## Slide 35: Δ-Y (delta-wye) Conversion
The following resistors form a Δ:
The following resistors form a Y:

## Slide 36: Δ-Y (delta-wye) Conversion
this Δ is equivalent to the Y if
this Y is equivalent to the Δ if

## Slide 37: Example: Δ-Y Conversion
How do we find the equivalent resistance of the following network? Convert a Δ to a Y

## Slide 38: Example: Δ-Y Conversion
use the Δ to Y equations
use standard serial and parallel combinations

## Slide 39: Summary
Can you explain these terms?
  Superposition Concept
  Practical Source
  Source Transformation
  Thevenin/Norton Circuits
  Δ-Y Conversion
Can you use them to simplify the analysis?

## Slide 40: In-class Exercise
Find maximum power of RL if it is connected across a and b terminals. What would be the value of RL itself?